## Slide 1: Monte-Carlo method and Parallel computing
An introduction to GPU programming Mr. Fang-An Kuo, Dr. Matthew R. Smith
NCHC Applied Scientific Computing Division

## Slide 2: NCHC
National Center for High-performance Computing.
3 Branches across Taiwan – HsinChu, Tainan and Taichung.
Largest of Taiwan’s National Applied Research Laboratories (NARL).
www.nchc.org.tw
2

## Slide 3: NCHC
Our purpose:
  Taiwan’s premier HPC provider.
  TWAREN: A high speed network across Taiwan in support of educational/industrial institutions.
  Research across very diverse fields: Biotechnology, Quantum Physics, Hydraulics, CFD, Mathematics, Nanotechnology to name a few.
3

## Slide 4: Outline
An introduction to HPC machine in Taiwan
Parallel Computation
  General parallel computing on PC cluster/SMP machine
  Accelerated processing unit, GPU
  An introduction to Taiwan HPC Facilities
GPU programming CUDA : An example dot product
Monte-Carlo method
Summany

## Slide 5
Most popular Parallel Computing Method
MPI/PVM
OpenMP/Posix Thread
Others , like CUDA

## Slide 6: MPI (Message Passing Interface)
An API specification that allows processes to communicate with one another by sending and receiving messages.
A MPI parallel program is running on a distributed memory system.
The principal MPI–1 model has no shared memory concept, and MPI–2 has only a limited distributed shared memory concept.

## Slide 7: OpenMP (Open Multi-Processing)
An API that supports multi-platform shared memory multiprocessing programming in C, C++, and Fortran.
A hybrid model of parallel programming can run on a computer cluster using both OpenMP and MPI.

## Slide 8: GPGPU
GPGPU = General scientific Programming on Graphics Processing Units.
Massively parallel computation using GPU is a cost/size/power efficient alternative to conventional high performance computing.
GPGPU has been long established as a viable alternative with many applications…

## Slide 9: GPGPU
CUDA (Compute Unified Device Architecture)
CUDA is a C-like GPGPU computing language helps us do general propose computations on GPU.
Computing card
Gaming card

## Slide 10
HPC Machine in Taiwan
ALPS(42th of Top 500)
IBM1350
SUN GPU cluster
Personal SuperComputer

## Slide 11: ALPS(御風者)
ALPS(Advanced Large-scale Parallel Supercluster, 42th of Top 500 SuperComputers) has 25600 cores and provides 177+ Teraflops
Movie : http://www.youtube.com/watch?v=-8l4SOXMlng&feature=player_embedded

## Slide 12: HPC Machine
Our Facilities:
  IBM1350 (iris) - > 500 nodes
  (Mixed Groups of Woodcrest
  and newer Xeon Intel processors)
  HP Superdome, Intel P595
  Formosa Series of Computers:
  Homemade supercomputers, built to custom by NCHC. Currently: Formosa III,IV just came online, Formosa V are under design.
12

## Slide 13: Network connection
InfiniBand 4x QDR – 40Gbps, average 1 latency
InfiniBand card

## Slide 14: Hybrid CPU/GPU @ NCHC (I)
14
Notes: 14

## Slide 15: Hybrid CPU/GPU @ NCHC (II)
15
Notes: 15

## Slide 16: My colleague’s new toy

## Slide 19
GPGPU Language
- CUDA
Hardware Architecture
CUDA API
Example

## Slide 20: GPGPU
NVIDIA GTX460
*http://www.nvidia.com/object/product-geforce-gtx-460-us.html
20
Graphics card version | GTX 460 1GB GDDR5 | GTX 460 768MB GDDR5 | GTX 460 SE
CUDA Cores | 336 | 336 | 288
Graphics Clock (MHz) | 675 MHz | 675 MHz | 650 MHz
Processor Clock (MHz) | 1350 MHz | 1350 MHz | 1300 MHz
Texture Fill Rate (billion/sec) | 37.8 | 37.8 | 31.2
Single Precision floating point performance | 0.9 TFlops | 0.9 TFlops | 0.74 TFlops

## Slide 21: GPGPU
Form Factor | 10.5" x 4.376", Dual Slot
# of Tesla GPUs | 1
# of Streaming Processor Cores | 240
Frequency of processor cores | 1.3 GHz
Single Precision floating point performance (peak) | 933 GFlops
Double Precision floating point performance (peak) | 78 GFlops
Floating Point Precision | IEEE 754 single & double
Total Dedicated Memory | 4 GDDR3
Memory Speed | 1600MHz
Memory Interface | 512-bit
Memory Bandwidth | 102 GB/sec
NVIDIA Tesla C1060*
*http://en.wikipedia.org/wiki/Nvidia_Tesla

## Slide 22: GPGPU
# of Tesla GPUs | 4
# of Streaming Processor Cores | 960 (240 per processor)
Frequency of processor cores | 1.296 to 1.44 GHz
Single Precision floating point performance (peak) | 3.73 to 4.14 TFlops
Double Precision floating point performance (peak) | 311 to 345 GFlops
Floating Point Precision | IEEE 754 single & double
Total Dedicated Memory | 16 GDDR3
Memory Interface | 512-bit
Memory Bandwidth | 408 GB/sec
Max Power Consumption | 800 W (typical)
NVIDIA Tesla S1070*

## Slide 23: GPGPU
Form Factor | 10.5" x 4.376", Dual Slot
# of Tesla GPUs | 1
# of Streaming Processor Cores | 448
Frequency of processor cores | 1.15 GHz
Single Precision floating point performance (peak) | 1030 GFlops
Double Precision floating point performance (peak) | 515 GFlops
Floating Point Precision | IEEE 754-2008 single & double
Total Dedicated Memory | 6 GDDR5
Memory Speed | 3132MHz
Memory Interface | 384-bit
Memory Bandwidth | 150 GB/sec
NVIDIA Tesla C2070*
*http://en.wikipedia.org/wiki/Nvidia_Tesla

## Slide 24: GPGPU
We have the increasing popularity of computer gaming to thank for the development of GPU hardware.
History of GPU hardware lies in support for visualization and display computations.
Hence, traditional GPU architecture leans towards an SIMD parallelization philosophy.

## Slide 25: The CUDA Programming Model

## Slide 26
GPU Parallel Code (Friendly version)
1. Allocate memory on HOST

## Slide 27
2. Allocate memory on DEVICE
Memory Allocated (h_A, h_B)
h_A properly defined
GPU Parallel Code (Friendly version)

## Slide 28
3. Copy data from HOST to DEVICE
Memory Allocated (h_A, h_B)
Memory Allocated (d_A, d_B)
h_A properly defined
GPU Parallel Code (Friendly version)

## Slide 29: GPU
GPU Parallel Code (Friendly version)
Memory Allocated (h_A, h_B)
Memory Allocated (d_A, d_B)
d_A properly defined
4. Perform computation on device
h_A properly defined

## Slide 30
Memory Allocated (h_A, h_B)
Memory Allocated (d_A, d_B)
d_A properly defined
5. Copy data from DEVICE to HOST
h_A properly defined
Computation OK (d_B)
GPU Parallel Code (Friendly version)

## Slide 31
Memory Allocated (h_A, h_B)
Memory Allocated (d_A, d_B)
d_A properly defined
h_A properly defined
Computation OK (d_B)
h_B properly defined
6. Free memory on HOST and DEVICE
GPU Parallel Code (Friendly version)

## Slide 32
Memory Allocated (h_A, h_B)
Memory Allocated (d_A, d_B)
d_A properly defined
h_A properly defined
Computation OK (d_B)
h_B properly defined
Complete
Memory Freed (h_A, h_B)
Memory Freed (d_A, d_B)
GPU Parallel Code (Friendly version)

## Slide 33: GPU Computing Evolution
NVIDIA CUDA GPU
parallel execution through cache
H2D
D2H
Host
Device
Memory transport, Host to Device (H2D)
Kernel execution
Memory transport, Device to Host (D2H)
Set a GPU Device ID in Host
The procedure of CUDA program execution
Notes: CPU,GPGPU,Nvidia GPU的資料傳遞,與處理過程說明

## Slide 35
Hardware
Software(OS)
Computer Core
Threads
L1/L2/L3 Cache
Register(local memory)/Data cache/Instruction prefetch
Hyper Threading/ Core overlapping
:
1 Core
Thread 1
Thread 2

## Slide 36: GPGPU
NVIDIA C1060 GPU architecture
Jonathan Cohen, Michael Garland, "Solving Computational Problems with GPU Computing," Computing in Science and Engineering, 11 [5], 2009.
Global memory

## Slide 39
Globel memory, non-cache
64K
16K/48K
Register
G80 : 8K
GT200 : 16K
Fermi : 32K
6GB, Telsa 2070
Notes: 新舊版本SM的內部記憶體比較

## Slide 40: CUDA code
The application runs on the CPU (host)‏
Compute intensive parts are delegated to the GPU (device)‏
These parts are written as C functions (kernels)‏
The kernel is executed on the device simultaneously by N threads per block (N<=512, or N<=1024 only for Fermi device)

## Slide 41
Compute intensive tasks are defined as kernels
The host delegates kernels to the device
The device executes a kernel with N parallel threads
Each thread has a thread ID, a block ID
The thread/block ID is accessible in a kernel via the threadIdx/blockIdx variable
The CUDA Programming Model
threadIdx
blockIdx
Thread

## Slide 42
CUDA Thread (SIMD) vs. CPU serial calculation
  CPU version
  GPU version
Thread 1
Thread 1
Thread 2
Thread 3
Thread 4
Thread 9
Notes: SIMT模型介紹

## Slide 43: Dot product via C++
In general, using a “for loop” via one thread in CPU computing.
SISD (Single Instruction Single Data)

## Slide 44: Dot product via CUDA
Using a “parallel loop” via many threads in GPU computing.
SIMD (Single Instruction Multiple Data)

## Slide 45: CUDA API

## Slide 46: The CUDA API
Minimal extension to C
  i.e. CUDA is a C-like computer language.
Consists of a runtime library
  CUDA Header file
  Host component: runs on host
  Device component: runs on device
  Common component: runs on both
    Only those C functions can run on device that are included in this component

## Slide 47: CUDA Header file
cuda.h
  Include cuda modulo.
cuda_runtime.h
  Include cuda runtime api.

## Slide 48: Header file
#include "cuda.h“
CUDA Header file
#include "cuda_runtime.h“
CUDA Runtime API

## Slide 49: Device selection (initialize GPU device)
Device Management
  cudaSetDevice()‏
    Initial GPU code
    Sets the device to be used
    MUST be set before calling any __global__ function
    Device 0 used by default

## Slide 50: Device information
See deviceQuery.cu in the deviceQuery project
cudaGetDeviceCount (int* count)‏
cudaGetDeviceProperties (cudaDeviceProp* prop)‏
cudaSetDevice (int device_num)‏
  Device 0 set be default

## Slide 51: Initialize CUDA Device
cudaSetDevice(0);
To
initialize the GPU device ID=0.
Maybe ID=0,1,2,3, or others in multiGPU environment .
cudaGetDeviceCount(&deviceCount);
Get the total number of GPU device
Notes: Dot0.cu

## Slide 52: Memory allocation in Host
Method I
Method II
Create these variables(mean its name) in program register and allocate system memory to the variable.
First Create these variables in program register.
Second, allocate system memory to these variables by Pageable mode

## Slide 53: Memory allocation in Host
Method III
First, Create some variables(its names) in Host
Second, Allocate GPU device memory to these variables of Host by Pinned memory.
Notes: Dot1.cu

## Slide 54: Memory allocation in Device
data1 <> gpudata1
data2 <> gpudata2
sum <> result (array)
RESULT_NUM is equal to the block number
Notes: Dot2.cu

## Slide 55: Memory Management
Memory transfers in both Host and Devcie
cudaMemcpy( void* dst, const void* src, size_t count, enum cudaMemcpyKind kind)
  Copies count bytes from the memory area pointed to by src to the memory area pointed to by dst,
  where kind is one of cudaMemcpyHostToHost, cudaMemcpyHostToDevice, cudaMemcpyDeviceToHost, or cudaMemcpyDeviceToDevice specifies the direction of the copy
  The memory areas may not overlap
  Calling cudaMemcpy() with dst and src pointers that do not match the direction of the copy results in an undefined behavior.

## Slide 56: Memory Management
Pointer : dst,src
Integer : count
Memory transfers from Device(dst) to Host(src)
  E.g. cudaMemcpy(dst, src, count, cudaMemcpyDeviceToHost)
Memory transfers from Host(src) to Device(dst)
  E.g. cudaMemcpy(dst, src, count, cudaMemcpyHostToDevice)

## Slide 57: Memory copy
Host to Device
Device to Host
Notes: Dot3.cu

## Slide 58: Device component
Extensions to C
  4 extensions
    Function type qualifiers
      __global__ void , __device__ , __host__
    Variable type qualifiers
    Kernel calling directive
    5 built-in variables
  Don’t suppose recursion in kernel function ( __device__ , __global__ )
Notes: 如何定義function 是屬於device還是host還是共有的

## Slide 59: Function type qualifiers
__global__ void
__device__
__host__
: GPU Kernel
: GPU Function

## Slide 60: Variable type qualifiers
__device__
  Resides in global memory
    Lifetime of the application
    Accessible from
      All threads in the grid
  Can be used with __constant__

## Slide 61: Variable type qualifiers
__constant__
  Resides in constant memory
    Lifetime of the application
    Accessible from
      All threads in the grid
      Host
  Can be used with __device__

## Slide 62: Variable type qualifiers
__shared__
  Resides in shared memory
    Lifetime of the block
    Accessible from
      All threads in the block
  Can be used with __device__
  Values assigned to __shared__ variables are guaranteed to be visible to other threads in the block only after a call to __syncthreads()‏

## Slide 63
Shared memory in a block/thread of GPU Kernels

## Slide 64: Variable type qualifiers - caveat
__constant__ variables are read only from device code
  Can be set through host
__shared__ variables cannot be initialized on declaration
Unqualified variables in device code are created in registers
  Large structures may be placed in local memory, SLOW

## Slide 65: Kernel calling directive
Must for calls to __global__ functions
Specifies
  Number of threads that will execute the function
  Amount of shared memory to be allocated per block, optional

## Slide 66: Kernel execution
Maximum number of threads is 512 (Fermi : 1024)
2D blocks/ 2D threads

## Slide 67: The CUDA API
Extensions to C
  4 extensions
    Function type qualifiers
      __global__ void , __device__ , __host__
    Variable type qualifiers
    Kernel calling directive
    5 built-in variables
  Don’t suppose recursion in kernel function ( __device__ , __global__ )

## Slide 68: 5 built-in variables
gridDim
  Of type dim3
  Contains grid dimensions
  Max : 65535 x 65535 x 1
blockDim
  Of type dim3
  Contains block dimensions
  Max : 512x512x64
  Fermi : 1024x1024x64

## Slide 69: 5 built-in variables
blockIdx
  Of type uint3
  Contains block index in the grid
threadIdx
  Of type uint3
  Contains thread index in the block
  Max : 512, Fermi : 1024
warpSize
  Of type int
  Contains #threads in a warp

## Slide 70: 5 built-in variables - caveat
Cannot have pointers to these variables
Cannot assign values to these variables

## Slide 71: CUDA Runtime component
Used by both host and device
Built-in vector types
  char1, uchar1, char2, uchar2, char3, uchar3, char4, uchar4, short1, ushort1, short2, ushort2, short3, ushort3, short4, ushort4, int1, uint1, int2, uint2, int3, uint3, int4, uint4, long1, ulong1, long2, ulong2, long3, ulong3, long4, ulong4, float1, float2, float3, float4, double2
  Default constructors float a,b,c,d; float4 f4 = make_float4 (a,b,c,d); // f4.x=a f4.y=b f4.z=c f4.w=d

## Slide 72: CUDA Runtime component
Built-in vector types
  dim3
    Based on uint3
    Uninitialized values default to 1
Math functions
  Full listing in Appendix B of programming guide
  Single and Double (sm>= 1.3) precision floating point functions

## Slide 73: Compiler & optimization

## Slide 74: The NVCC compiler (Linux/Windows command mode)
Separates device code and host code
Compiles device code into binary, cubin object
Host code is compiled by some other tool, e.g. g++
Nvcc <file> -o <output file> -lcuda

## Slide 75: Memory optimizations
cudaMallocHost() instead of malloc()‏
cudaFreeHost() instead of free()‏
Use with caution
  Pinning too much memory leaves little memory for the system

## Slide 76: Synchronization

## Slide 77: Synchronization
All kernel launches are asynchronous
  Control returns to host immediately
  Kernel executes after all previous CUDA calls have completed
  Host and device can run simultaneously

## Slide 79: Synchronization
cudaMemcpy() is synchronous
  Control returns to host after copy completes
  Copy starts after all previous CUDA calls have completed
cudaThreadSynchronize()
  Blocks until all previous CUDA calls complete

## Slide 80: Synchronization
__syncthreads or cudaThreadSynchronize ?
__syncthreads()‏
  Invoked from within device code
  Synchronizes all threads in a block
  Used to avoid inconsistencies in shared memory
cudaThreadSynchronize()‏
  Invoked from within host code
  Halts execution until device is free

## Slide 81: Dot product via CUDA

## Slide 82: CUDA programming – step-by-step
Initialize GPU device
Memory allocation on CPU and GPU
Initialize data on host/CPU and Device/GPU
  Memory copy
Build your CUDA Kernels
Submit kernels
Receive these results from GPU device

## Slide 83: Dot product in C/C++

## Slide 84: One block and one thread
Synchronize in Host
Block=1, thread=1
Timer
Output the result
Notes: Dot4.cu

## Slide 85: One block and one thread
CUDA kernel : dot
Notes: Dot4.cu

## Slide 86: One block and many threads
Use 64 threads in one block
Notes: Dot5.cu

## Slide 87
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
0
1
2
3
4
5
6
7
Thread ID :
data :
Parallel loop for dot product

## Slide 88: Reduction using shared memory
Add ‘shared memory’
Reduction by using shared memory
Initial the shared memory by 64 threads (tid)
Synchronize all threads in a block
Notes: Dot5.cu

## Slide 89: Parallel Reduction
Tree-based approach used within each thread block
Need to be able to use multiple thread blocks
  To process very large arrays
  To keep all multiprocessors on the GPU busy
  Each thread block reduces a portion of the array
But how do we communicate partial results between thread blocks?
4
7
5
9
11
14
25
3
1
7
0
4
1
6
3
From CUDA SDK ‘reduction’

## Slide 90: Parallel Reduction: Interleaved Addressing
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values (shared memory)
0
2
4
6
8
10
12
14
11 | 1 | 7 | -1 | -2 | -2 | 8 | 5 | -5 | -3 | 9 | 7 | 11 | 11 | 2 | 2
Values
0
4
8
12
18 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 4 | -3 | 9 | 7 | 13 | 11 | 2 | 2
Values
0
8
24 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 17 | -3 | 9 | 7 | 13 | 11 | 2 | 2
Values
0
41 | 1 | 7 | -1 | 6 | -2 | 8 | 5 | 17 | -3 | 9 | 7 | 13 | 11 | 2 | 2
Values
Thread IDs
Step 1 Stride 1
Step 2 Stride 2
Step 3 Stride 4
Step 4 Stride 8
Thread IDs
Thread IDs
Thread IDs
From CUDA SDK ‘reduction’

## Slide 91
10 | 1 | 8 | -1 | 0 | -2 | 3 | 5 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values (shared memory)
0
1
2
3
4
5
6
7
8 | -2 | 10 | 6 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values
0
1
2
3
8 | 7 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values
0
1
21 | 20 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values
0
41 | 20 | 13 | 13 | 0 | 9 | 3 | 7 | -2 | -3 | 2 | 7 | 0 | 11 | 0 | 2
Values
Thread IDs
Step 1 Stride 8
Step 2 Stride 4
Step 3 Stride 2
Step 4 Stride 1
Thread IDs
Thread IDs
Thread IDs
From CUDA SDK ‘reduction’

## Slide 92: Many blocks and many threads
64 blocks and 64 threads per block
Sum all result from these blocks
Notes: Dot6.cu

## Slide 93: Dot Kernel

## Slide 94: Reduction kernel : psum
Notes: Dot6.cu

## Slide 95: Monte-Carlo Method via CUDA
Pi estimation

## Slide 96
Figure 1

## Slide 97
Ux, Uy are two random variables from Uniform [0,1] , these sampling data of Ux and Uy can be written as
The indicator Function will be defined by
Assuming the following

## Slide 98
Monte-Carlo Sampling
Points An(Ux,Uy) are samples in the area of figure 1, we can estimate circle measure by the probability value which a point is inside of the circle.
The probability value P = =

## Slide 99
Algorithm of CUDA
Everything is as the same as dot product.

## Slide 100
CUDA codes (RNG on CPU and GPU)
* Simulation (Statistical Modeling and Decision Science) (4th Revised edition)

## Slide 101
CUDA codes (Sampling function)

## Slide 102
CUDA codes (Pi)

## Slide 103: Questions ?

## Slide 104: For more information, contact:
Fang-An Kuo (NCHC)
Email: mathppp@nchc.narl.org.tw mathppp@gmail.com