## Slide 1: Overview of Sensor Networks
499415130 王維寬
601415010 林奕丞
601441045 鄭賜福

## Slide 2: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 3: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 4: Introduction
The science and technology are deeply intertwined.
The influence on the WSNs from technology :
    Computing Capacity
    Radios
    Mechanical Structure

## Slide 5: WSN’s constraints
Processing Speed
Storage Capacity
Communication Bandwidth

## Slide 6
Energy Consideration:
  Because of the long-periods operation and wireless, the energy resources limit overall operation.
  The device’s components, including the radio, will likely be turn off most of the time.
Self-adjustment
Because manually configuring large networks of small
devices is impractical.

## Slide 7: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 8: Sensor network applications
Monitoring space
Monitoring things
Monitoring the interactions of things with each other and the encompassing space

## Slide 9
Nesting seabird habitats
Microclimate chaparral transects
Conducting analogous studies of contaminant propagation
Building comfort
Intrusion detection
Environmental monitoring

## Slide 10
Monitoring the microclimate throughout the volume of redwood trees
Climatic factor :
    Photosynthesis
    Water and nutrient transport
    Growth patterns
Environmental monitoring

## Slide 11: Environmental monitoring
WSN climate data. The WSN samples climate data every ﬁve minutes and computes an average temperature at each elevation.

## Slide 12: Environmental monitoring
Wireless sensor node for environmental monitoring. An entire wireless weather station ﬁts in a tube about the size of a ﬁlm canister.

## Slide 13: Motion monitoring
Physical structure:
    Vibration
    Acoustic emissions
    Response to stimuli
WSN can performing local process at each device and transporting the data continuously to operations staff

## Slide 14: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 15: Embedded Network Technology
WSNs merge a wide range of information technology that spans hardware, systems software, networking, and programming methodologies.

## Slide 16: WSN hardware
Data storage
Sensors
ADC
Data transceiver
Controller
Energy source (Ex :solar cells, vibration of windows, air condition ducts)

## Slide 17: WSN hardware
Low-power microcontroller have limited storage, typically less than 10K bytes of RAM .

## Slide 18: Microsensors
Physical phenomena Voltage (change resistance)
Binary number
Microelectromechanical systems(MEMS)
High-precision piezoelectric accelerometers(expensive)
Sufficient-precision MEMS(cheap)

## Slide 19: Microradios
Consumption
Wireless LANs and cell phones : hundreds of milliwatts
WSN radios : 20 milliwatts(range : tens of meters)
Communication remains one of the most energy-consuming operations.
    → 1 bit costs as much as 1000 instructions.

## Slide 20: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 21: System Challenge
The network must allocate limited hardware to multiple concurrent activities(sampling sensors, processing and streaming data)

## Slide 22: Tiny OS
Focusing on structured interaction with the physical world, rather than on complex human interactivity.
Each component handles certain events and signals actions in other components, but they never consume processor cycles while waiting for future events.

## Slide 23: Lower level of network
Acquiring the radio channel
Framing data stream into packet
Error coding
Channel scheduling
Detecting and process the incoming packets

## Slide 24: Higher level of network
Buffer management
Authentication
Multiplexing the network
Receiving and processing a stream
Delivering important notification

## Slide 25: Network sensor platforms
Berkeley Motes :
Sensing capacities
Communication radio
Computation unit
Power source
Intel iMote
ARM processor
Storage
Radio : The Bluetooth standard

## Slide 26: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 27: Self-organized Networks
A network consists of many nodes, each with multiple links connecting to other nodes. Information moves hop by hop along a route from the point of production to the point of use.

## Slide 28: Connectivity
When one node transmits
the link layer listens on the channel and transmits only
when the channel is clear.
When not transmitting
nodes sample the channel and scan for a special symbol
at the start of a packet that also lets the receiver align
itself with the sender’s time.

## Slide 29: Dissemination and data collection
the network uses the identifying information to detect and suppress duplicates.
The flooding protocols use various techniques to avoid contention and minimize redundant transmissions
The root can be a gateway to a more powerful network or an aggregation point within the sensor network, as determined by some higher-level task.

## Slide 30: Usage of dissemination
Issuing commands
Convey alarms
Configuring and tasking the network
Establishing routes

## Slide 31: Reliability
Increasingly, sensor networks will deploy disruption tolerant networking(DTN) approaches in which they transfer bundles of data reliably, hop by hop.

## Slide 32: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 33: Conserving Power And Bandwidth
Communication, usually the most energy-intensive operation a node performs, must contend for a share of limited bandwidth.
Performing aggregation within the network can reduce communication.
Compression and scheduling also can conserve energy at lower layers.

## Slide 34: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 35: Privacy
Fortunately, this area has become an active focus of research while the technology is still in its early stages

## Slide 36: Outline
Introduction
Sensor Network Applications
Embedded Network Technology
System Challenge
Self-organized Networks
Conserving Power And Bandwidth
Privacy
In This Issue

## Slide 37: In This Issue
The articles in this special issue span novel sensor network applications, embedded network technology, and systems design challenges.
Articles:
    Date gather
    Traffic
    Detect sniper
    Low power
    Curriculum

## Slide 38: Conclusion
WSNs appear to represent a new class. They follow the trends of size, number, and cost, but have a markedly different function. Rather than being devoted to personal productivity tasks, WSNs make it possible to perceive what takes place in the physical world in ways not previously possible.

## Slide 39: END
Thanks for your attention!!