## Slide 1: SPEED: A Stateless Protocol for Real-Time Communication in Sensor Networks
Tian He, John A Stankovic , Chenyang Lu, Tarek Abdelzaher
International Confernece on Distributed Computing Systems (ICDCS-23), Providence, RI, USA, pages 46-55, May 2003.
第二組 601430002黃霈哲 601430013黃煌彬

## Slide 2: Outline
CH1: Introduction
CH2: SPEED
CH3: Evaluation
CH4: Multimodal Activity Based Localisation

## Slide 3: CH1 Introduction
A real-time communication protocol for sensor networks, called SPEED.
Real-time constraints may exist
  Surveillance system
  Battlefield monitoring
  Earthquake response system
  Smart hospitals

## Slide 4: CH1 Introduction
three types of communication patterns
  unicast
  area-multicast
  area-anycast
A protocol SPEED that supports soft real-time communication based on feedback control and stateless algorithms for large-scale sensor networks.

## Slide 5: CH1 Introduction
evaluate SPEED via simulation using GloMoSim and compare it to five other ad hoc routing protocols: DSR, AODV, GF and two scaled down versions of SPEED.

## Slide 6: CH2: SPEED

## Slide 7: CH2 State of the Art
Location based routing algorithm
  Greedy Perimeter Stateless Routing (GPSR)
  Geographic distance routing (GEDIR)
  Location-Aided Routing (LAR)

## Slide 8: CH2 State of the Art
Real-Time protocol
  Service Differentiation in Stateless Wireless Ad Hoc Networks (SWAN)
  Real-Time Communication Architecture for Large-Scale Wireless Sensor Networks (RAP)
  A Transmission Control Scheme for Media Access in Sensor Networks

## Slide 9: CH2 State of the Art
Reactive routing algorithm
  Ad-hoc On Demand Distance Vector Routing (AODV)
  Dynamic Source Routing in Ad Hoc Wireless Networks (DSR)

## Slide 10: CH2 Design Goals
Stateless Architecture
Soft Real-Time
Minimum MAC Layer Support
QoS Routing and Congestion Management
Traffic Load Balancing
Localized Behavior
Void Avoidance

## Slide 11: CH2 SPEED Protocol
An API
A neighbor beacon exchange scheme
A delay estimation scheme
The Stateless Non-deterministic Geographic For-warding algorithm (SNGF)
A Neighborhood Feedback Loop (NFL)
Backpressure Rerouting
Last mile processing

## Slide 12: CH2 SPEED Protocol

## Slide 13: CH2 SPEED - API
AreaMulticastSend (position, radius, packet)
  It sends a copy of the packet to every node inside the specified area.
AreaAnyCastSend (position, radius, packet)
  This service sends a copy of the packet to at least one node inside the specified area.
UnicastSend (Global_ID, packet)
  The node identified by Global ID will receive the packet with a speed above a certain desired value.
SpeedReceive ( )

## Slide 14: CH2 SPEED - Packet Format
PacketType: The type of communication: Area Multicast, AreaAnyCast or Unicast.
Global_ID: Only used in Unicast communication to identify a destination node.
Destination Area: Describes a three-dimensional space with a center point and radius in which the packets are destined.
TTL: Time To Live field is the hop limit used for last mile processing.
Payload.

## Slide 15: CH2 SPEED - SNGF
The Neighbor Set of Node i: NSi is the set of nodes that are inside the radio range of node I .
The Forwarding Candidate Set of Node i: A set of nodes that belong to Nsi and are closer to the destination.

## Slide 16: CH2 SPEED - SNGF

## Slide 17: CH2 SPEED – SNGF_Rule
Packets are forwarded only to the nodes that belong to the FSi (Destination). If there is no node inside the FSi (Destination), packets are dropped and backpressure.
SPEED divides the neighbor nodes inside FSi (Destination)into two groups.
  Relay speeds > Ssetpoint
  Relay speeds < Ssetpoint (NFL)

## Slide 18: CH2 SPEED – SNGF_Rule
The forwarding candidate is chosen from the first group, and the neighbor node with highest relay speed has a higher probability to be chosen as the forwarding Node.
If there are no nodes belonging to the first group, a relay ratio is calculated based on the Neighborhood Feedback Loop (NFL)

## Slide 19: CH2 SPEED - NFL (MAC Layer Feedback)
Delay Estimation: Delay= Round Trip Time – Receiver Side Processing Time
On/Off Switch
Back-Pressure Rerouting
Last Mile Process
SNGF
Backpressure
Rerouting
NFL
Beacon
Exchange
API
UniCast
MultiCast
AnyCast
MAC
Delay
Estimation
Neighbor
Table
Relay Ratio Control

## Slide 20: CH2 SPEED - Backpressure Rerouting based on MAC Layer Feedback & SNGF
2
3
5
9
10
7
Delay
11
Boo
SPEED
20
110
30
115
Node 5's NT
Delay
0.5s
0.1s
0.4s
0.1s
ID
9
7
10
3
Packet
Packet
Source
Destination

## Slide 21: CH2 SPEED - Backpressure Rerouting based on MAC Layer Feedback & SNGF
2
3
5
9
10
7
Delay
Boo
ID Delay
5 0.5S
2 0.1S
4 0.1S
Node 3's NT
4
11
6
1
3
ID Delay
5 0.1S
7 0.4S
Node 6's NT
12
Packet 1
Packet 1
Beacon
Packet 2
Packet 2
Packet 2
Packet 2
Packet 2
Packet (to 4)

## Slide 22: CH2 SPEED Last Mile Process
AreaMulticastSend(Center position, radius, deadline, packet)
AreaAnyCastSend(Center position, radius, deadline, packet)
UnicastSend(Global_ID,deadline,packet)
SpeedReceive()

## Slide 23: CH3 Evaluations

## Slide 24: CH3 Evaluations - Congestion Avoidance

## Slide 25: CH3 Evaluations - Control Overhead
Control Packets vs. Congestion-Level

## Slide 26: CH3 Evaluations - Energy Consumption
Energy Consumed vs. Congestion-Level
0
5
10
15
20
25
30
35
40
0
10
20
30
40
50
60
70
80
90
100
Rate (P/S)
AODV
DSR
SPEED
GF
SPEED-S
SPEED-T
Energy Consumption

## Slide 27: CH3 Evaluations - Void Avoidance
70%
75%
80%
85%
90%
95%
100%
15.5
13.9
12.6
11.4
10.4
9.5
8.7
8.0
Density (nodes per radio circle)
DSR
SPEED
GF
SPEED-S
SPEED-T
Delivery Rate