## Slide 1
能源科技與環境概論 太陽能電池導論
Hsing-Yu Tuan (段興宇）
Department of Chemical Engineering, National Tsing-Hua University

## Slide 2: References
太陽電池 solar cells 黃惠良、曾百亨
Optoelectronics and photonics priciples and practices, S.O. Kasap 1999
Handbook of photovoltaic science and engineering Antonio Luque

## Slide 6: Solar cells
Solar light in
Electricity out

## Slide 7: The request for solar energy
人類用電的使用量只會越來越高，而太陽能電池的
需求也會與日劇增
當達到黃金交叉時，太陽能電池
市場會有爆炸性的發展。

## Slide 9: Video

## Slide 10: Solar light spectrum

## Slide 11: Energy conversion of light
(wave factor)
A light with a wavelength of 1100 nm corresponds to 1.12 eV

## Slide 12: Generate electrons from materials by photons
Separation of the
electron-hole
pair
Conduction band
or HOMO
Valence band
or LUMO
Conduction band
or HOMO
Valence band
or LUMO
electron
pair
So, materials used for solar cell application need to have discrete energy
gap for photogeneration of electron-hole pair
excited state

## Slide 14
Inorganic materials: Insulator, semiconductor and metal
Streetman p62
Insulator Semiconductor Metal
conduction band
valance band
> 5 eV

## Slide 15: Elemental and Compound Semiconductors
 |  | 5 B | 6 C | 7 N | 8 O
 |  | 13 Al | 14 Si | 15 P | 16 S
29 Cu | 30 Zn | 31 Ga | 32 Ge | 33 As | 34 Se
47 Ag | 48 Cd | 49 In | 50 Sn | 51 Sb | 52 Te
I II III IV V VI
15
Notes: 15
You have heard many good things from me about CIGS solar cell. From here, I would like to give a brief introduction of CIGS material and its properties. CIGS is a I-III-VI compound semiconductor derived from II-VI compound. The group II element is replaced by group I and group III elements. Therefore, the I-III-VI compound has the atomic ratio of 1:1:2. Like other compound semiconductors, the elements belongs to the same group can be substituted to form solid solution such as Cu-In-Ga-Se quaternary compound or even Cu-In-Ga-Se-S pentanary compounds.

## Slide 16
Silicon
CIGS
CdTe
GaAs
Inorganic Semiconductors

## Slide 17: Conducting polymer

## Slide 18: Or dyes

## Slide 19: Various types of solar cells
solar cells
silicon
compound
organic
crystalline
thin film amorphous
single crystalline
polycrystalline
III-V(GaAs)
poly crystalline
thin film
dye sensitized
polymer
single crystalline
CIGS
CdTe

## Slide 20: Solid materials : types

## Slide 21: Solar cell Efficiencies
太陽電池材料種類 |  |  | 量產電池 轉換效率 | 量產模組 轉換效率 | 我國主要廠商
矽 | 矽晶片型 | 單晶 | ~18% | ~16% | 茂迪、昱晶、新日光、益通等………
 |  | 多晶 | ~16.8% | ~15% | 茂迪、昱晶、新日光、益通等………
 | 薄膜矽 | 非晶、非晶/微晶堆疊 | 8~13% | 7~10% | 聯相、富陽、宇通、旭能等………
化合物半導體 | III-V族 | GaAs 砷化鎵 (晶片、薄膜型) | 18~30% | ~25% | 華宇、禧通、億芳等………
 | II-VI族 | CdTe銻化鎘 (薄膜型) | 12~15% | 10~12% | 我國無廠商投入
 | 多元化 合物 | CIGS銅銦鎵硒 (薄膜型) | 12~14% | 10~11% | 新能、綠陽、台積電等………
有機物 |  | DSSC 染料敏化 | 6~9% | ~6% | 台塑、永光、福盈等………

## Slide 23: Pick right materials as absorption layer
- Good absorption coefficient to harvest
light
- Suitable band gap

## Slide 24
Direct band gap and indirect band gap structure
-We prefer direct semiconductor materials
since they can absorb light more efficiently

## Slide 25: Absorption of semiconductors
-Si and Ge’s absorption coefficient
increase slowly with increased energy

## Slide 26
Theoretical maximum efficiency of a semiconductor
bandgap of semiconductor should not be wide in order to get higher
-Electrons in the valence band can absorb energy of Eg, 2 Eg, 3Eg, but the excess energy can not be transformed to electric energy but transform to heat  need higher Eg
-very narrow band gap material can absorb most wavelength from sun, but transformed energy is small.
Pick suitable Eg (eV)
(neither
wide nor narrow)
S(λ) =# of photons/area*time

## Slide 27
real ηmax is only around
30% due to loss of other facters
ηmax(%) vs Eg (eV) under AM1.5
Eg:
1.0 – 1.5 eV is the best range

## Slide 29
Semiconductor band, using Si as an example

## Slide 30: Doping of Si: increase the conductivity of intrinsic Si
Donors: P, As, Sb (Column V elements ) , n-type,  provide one additional electron
Acceptors: B, Ga, In, (Column III elements), p-type provide one additional hole
P+
B-
-
-weakly bound
-bonding strength EB~ 0.05 eV (Si bonding ~1.12 eV)
Donors EB Acceptors EB
Sb 0.039 eV B 0.045 eV
P 0.044 eV Al 0.057 eV
As 0.049 eV Ga 0.065 eV
In 0.16 eV
Ec
Ev
ED
0.044 eV (P)
0.057 eV (Al)
EA
Majority carrier - electron in a n-type material
hole in a p-type material
Minority carrier – hole in a n-type material
electron in a p-type material

## Slide 31: P-N junction

## Slide 32: A PN junction photovoltaic device
-incoming photon generate EHPs and
create current
-generated electrons and hole can
diffuse and drift in neural region and SCL, respectively
-Opencircuit voltage (Voc) develops between the terminals
of the device because the electrion reaches the
neutral n and p, respectively.
PN junction provide a
Depletion region in where an electric
field is created for drifting
electron and hole

## Slide 33
Device structure of a Si solar cell
Finger electrodes
p
n
Bus electrode
for current collection
- finger electrodes were made to allow light pass through the device
a thin antireflection coating on the surface reduces light reflection and allow more
lighte to enter the device
-surface texturization to for multiple light reflection and increase light path
0.2 μm
200 μm
In order to capture more light
surface texturization
Incident light
(1)
(2)
(3)

## Slide 34: Schematic of a semocnoductor solar cell

## Slide 35: Video

## Slide 36
IV curve of a solar cell
Voc (open circuit voltage)
-when output current approaches zero,
the voltage develops between two terminals
ideally Voc~Eg at 0K and inverse proportional
to temperature
Jsc (short-circuit current)
-like the device connect the device with metal circuit,
close to photogenerated current
FF (fill factor): We want FF close to 1

## Slide 37: Solar cell efficiency :an example
Chart: 
η=PMP /Pin x100%=FF*VocJsc/ Pin x100%
（輸出電功率/入射光功率)
P in =100 mW/cm2
PMP=VMP*JMP=0.55*5.9716=3.28mW/cm2
η =3.28/100*100%=3.28%
Voc=0.72 V
Jsc=7.1464 mA/cm2
FF=VMP*JMP/Voc*Jsc
=3.28/(0.72*7.14)=0.63
(0.55,5.9716)
VMP
JMP
Voc
Jsc
Voc: 開路電壓 (open circuit voltage), 當輸出電流趨近於零，相
對太陽電池兩電極端點沒有連接所得到的電壓
Jsc:短路電流(short circuit current)
如將照光的pn二極體兩端的金屬電極用金屬線連接, 造成短路, 此短路電流等於光電流
η and FF in this device ?

## Slide 38
Various losses of solar energy of a Si solar cell during processing
Silicon band gap is 1.1 eV, and
the device loses all photon energy
less than 1.1 eV
Voc is inverse proportional to
temperature, so not equals to Eg
Only 43.6% remaining!
Excessive photon energy
Near surface EHP recombination
Antireflection coating is not perfect
The highest efficient of a real
photovoltaic device that uses a
single crystal of Si
Is about 24.7% (澳洲新南威爾斯
大學）
device fabrication resistance

## Slide 39: Single/poly crystalline Si solar cell fabrication process
etch in a strong acidic
or alkaline solution
etch in a weak acidic
or alkaline solution
liquid glass containing P is distributed on one side of the wafer by spraying or spinningand heated
(the wafer are placed in a belt furnace
And heated about 900 °C
The reflectivity is still round 30%,H:SiNx is deposited
on the cell to reduce more the reflectivity
metal contacts are made by screen printing
Metallic contacts are heated and
Etch trough the antiflecton coating
P-type ingot
was cut

## Slide 40: Solar cells installation
DC power

## Slide 41: Next step of crystalline Si solar cell

## Slide 42
貳、發展現況(續)
五、我國太陽光電產業鏈
Installation：茂迪、台達電、廣運、友達、聯相、宇通、富陽、永盛能源、有成、綠能、大金、東城、冠宇宙、太陽動力、鼎鼎、聚恒、金華成、中國大陸電器、羅森、全面性、伸浦、崇越、統昱、永旭、台邦、傳典、高鋒、華旭環能、工易、耀能、上揚、錸德、光寶綠能、詠通、華城、亞力、駿成、曜晟、寶球、明宜、元太、伸浦、新世紀、金頓、海灣、泰新、安慶、昇暉、雄雞
System Parts：台玻、元璋、太美、城東、力鋼、元一、高鋒、法隆、泉鋼、盈正豫順、明碁材料、達方、台虹、碩禾、致嘉、台塑、暘益、台聚、新輝、昇貿、宏致、泰和、建和興、科宥
Equipment：均豪、廣運、欽揚、東遠、志聖、帆宣、北儒、翔勝、致茂、綠色
Product：亞通、東城、強而青、鯨威、日光能、茂迪、中國大陸電器、同昱、旭辰、旭邦、科宥、信合、千附、永炬、日曜、宇能、智柏、登陽 、誼成、森富國際、
100 Companies
Poly-
Silicon
Ingots/
Wafer
Solar Cell
PV Module
PV System & Installation
Solar Grade
Silicon
Si Ingot
& Wafers
Wafer-based Solar Cell
－Mono-Si, Multi-Si, GaAs
Thin-film Solar Cell
－a-Si/-Si, CIS,
－Dye Sensitized Solar Cell
CPV Solar Cell
PV
Modules
Installation
System Parts
－Inverter, BOS…
Equipment
Product
Up Stream
Mid Stream
Down Stream
Industry
Company
中美晶
綠能
合晶
統懋
峰毅
茂迪
旭晶能源
晶耀
達能
國碩
昱成光能
友達晶材
12 Companies
福聚太陽能
友達晶材
寶德能源
實聯能源
科冠
山陽科技
6 Companies
矽晶電池：茂迪、益通、旺能、昱晶、新日光、昇陽、茂矽、太陽光電、太極、燿華、長生能源、旭泓、亞崙、尚陽、強茂、樂福、聯景、元晶、英穩達、友達
矽薄膜電池：綠能、聯相、富陽、宇通、八陽、旭能
CIGS電池：綠陽、新能、太陽海、正峰新、亞化、威奈聯合、台積電
聚光型電池：全新、華上、禧通、台達電、晶電、宏捷、華旭、億芳、瀚昱、海德威、太聚、綠源、吉泰、亞飛、禾晶
DSSC：健鼎、福盈、永光、镸興、台塑
 54Companies
頂晶
知光
英懋達
生耀
科風
茂暘
錸德
有晴
大晶
全能
安集
茂鑫
強茂
有成
友達
綠晁
鼎笙
17Companies
歷年廠家數：
2005＝40
2006＝50
2007＝76
2008＝100
2009＝123
2010＞160

## Slide 43
歐洲與日本之電池產量由2006年市占率約30%下降至2011年的10%以下。
太陽光電生產基地持續向亞洲移動趨勢不變，中國大陸與臺灣生產比例近全球70%。
大陸挾其成本優勢與政策支持，成為全球最大製造國，2011年產值達2536億元人民幣。

## Slide 44: Thin film solar cell: use Si as an example
- required thickness of thin film solar cell is around 0.5 μm, 1/500 of that of wafer based solar cell
- material cost is very low

## Slide 45: Advantages of thin film solar cells
  1. low raw materials are required for fabrication
  2. light transmission is better
  3. more competitive price (CdTe, US$1 per watt ; First
  Solar, stock price is US$180 )
  4. frameless design
  5. Ideal for BIPV( building integrated photovoltaic)