## Slide 1
課程說明:
教育化工系的同學，使認識光電材料與光電元件的基礎及其製程，
俾便未來運用化學工程技術在這些相關的產業之中。
內容主要分為三大部分: 光電材料與元件基本原理, 無機光電材料與元件
、有機光電材料與元件。
任課教師:
段興宇教授 (ext: 42509, hytuan@che.nthu.edu.tw, Room 311)
Prof. Masaki Horie (ext: 33628, mhorie@mx.nthu.edu.tw, Room 510)
CHE 4940 Fundamentals of Opto electronic Materials and Devices
(光電材料與元件基礎 2 學分)

## Slide 2: 教學進度： I. 光電材料與元件基本原理: 段興宇教授 M7M8
上課日期 | 授課內容
2/22 | Class description
3/8 | Semiconductor fundamentals
3/15 | Principle of optoelectronic devices(I)
3/22 | Principle of optoelectronic devices (II)
3/29 | Principle of semiconductor-based solar cells
4/12 | Integrated circuit (IC) manufacturing processes
4/19 | Chemical vapor deposition (CVD)
4/26 | Midterm

## Slide 3: II有機光電材料與元件 Prof. Masaki Horie M7M8
上課日期 | 授課內容 (course content)
5/3 | Introduction of organic electronics
5/10 | Organic photovoltaic devices
5/17 | Organic field effect transistors
5/24 | Liquid crystal displays and organic light emitting diodes
5/31 | Organic materials for energy storage (capacitor, battery, and fuel cell)
6/7 | Molecular machines and devices
6/21 | Final exam

## Slide 4: 成績評定
Part I. 期中考, 50%.
教學方式
Lectures (power point presentations)
1.投影片PDF檔下載：http://mx.nthu.edu.tw/~hytuan/
2.助教：白睿宇 <kartdcard0115500@gmail.com>

## Slide 5: Overview of Integrated Circuits (IC) industry in Taiwan
中美晶、綠能
台積電（世界第一）、聯電、漢磊
聯發科等IC設計公司
台灣光罩
日月光
向外國購買

## Slide 6
Pizza vs microchip fabrication

## Slide 7: Integrated circuits (ICs)
Courtesy of wiki
- Combination of transistors, diodes, capacitors in a chip
Ultra large scale integration (ULSI) >1,000,000 components per chips
- Morre’s law: the number of transistors on a chip were doubling every 18 months
- Intel four core Itanium CPU- Tukwila has over 2 billion transistors on a chip

## Slide 9: Si, Si, Si, why Silicon???
Silicon has smallest carrier mobility
compared with Ge and GaAs.
Drawback of Ge
-Ge’s device easily to leak at high temp.
-GeO2 is water soluble
-melting point of Ge is only 937 C
Drawback of GaAs
-hard to get high quality and large size wafer
-need additional procedures to form dielectic
materials
Advantage of Si
Cheap raw materials, e.g., rock, sand,
second most abundant element on earth,
appear as SiO2
- High melting point: 1415C
- stable silicon oxide (SiO2) as dielectric materials

## Slide 10: Optoelectronic devices using semiconductors: Si、III-V、I-III-VI, many semiconductors are candidates
LED (light emitting diodes)
Laser
Solar cell
Photodetector

## Slide 11: The band gap of semiconductor optoelectronic materials corresponding to a optical spectrum
E= hc/λ
E=1.24/ λ (eV)
When E: electron volts
λ:μm
direct band gap materials
Compound (II-VI, III-V, IV-VI) semiconductors

## Slide 12: LED – basic manufacturing processes
經,3-76
Similar manufacturing process could be also applied to laser, solar cell industry

## Slide 13
友達光電-國內最大的面板廠
國立清華大學化學工程所博士 92D
曾任友達光電總經理陳來助博士
本系的系友
你們的學長
工學院 Next Power 講座、學生獎學金捐款
(一年一百萬、為期五年)

## Slide 14: 晶元光電-國內LED第一大廠
國立清華大學工業化學系學士 80B
國立清華大學化學工程所博士 85D
晶元光電董事長兼總經理
李秉傑博士
本系的系友
你們的學長
晶元光電講座、學生獎學金捐款 (一年一百萬、為期五年)

## Slide 15: 晶元光電-國內LED第二大廠
璨圓光電董事長 簡奉任博士
本系的系友
你們的學長
清大化工系友會會長
國立清華大學化學工程學系 85B

## Slide 16: 碩禾光電/國碩科技-太陽能材料大廠
國碩總經理 曾任碩禾光電副總經理
蔡禮全
本系的系友
你們的學長
國立清華大學化學工程學系 71B

## Slide 17: 聯華電子: 國內晶圓代工第二大廠
本系的系友
你們的學長
曾任聯電執行長
國立清華大學化學工程學系 80B